## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 12

## Slide 3: IP (Internetworking Protocol)
BLM3051
Data Communication and Computer Network - 12
Dr. Öğr. Üyesi Furkan ÇAKMAK
TCP/IP: 4-5 katman
Sockets
Transport Layer
  TCP (Transmission Control Protocol)
  UDP (User Datagram Protocol)
Package: Data with address info
Datagram: Packet that complies with the structure defined by IP

## Slide 4: IP (Internetworking Protocol) – Internet Layer
Connectionless Protocol
  No ACK
  No error handling
  Left to other layers
So, IP is also described as an unreliable protocol.
Basic Tasks of IP
  Defining datagrams
  Adding address info to datagrams
  Transferring data between the transport layer and network access layers
  Routing of datagrams
  Fragmentation of datagrams and Re-assembling of them.
Packets consist of 4 bytes addresses.
  Ex: 193.140.4.1
BLM3051
Data Communication and Computer Network - 12
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 5: IP (Internetworking Protocol) – IPv4
BLM3051
Data Communication and Computer Network - 12
Dr. Öğr. Üyesi Furkan ÇAKMAK
Host Addresses:
  11111111 -> Broadcast
  00000000 -> Network Address
  254 address left
Subnet
  Let's say a company has 35 terminals in Istanbul and 40 terminals in Ankara.
    Total 75 terminals.
    Is a class C address enough?
    Is a class C address too much?
  C Class IP Subnet Mask:
    255.255.255.192
      2 x Network Address
      62 ( x Host Address
  Does the number of hosts decrease using subnet?
    252 (2 subnet x 126 address/subnet)
    248 (4 subnet x 62 address/subnet)
    240 (8 subnet x 30 address/subnet)

## Slide 6: IP (Internetworking Protocol) – Special IP Addresses and NAT(Network Address Translation)
Special Purpose IP Address
  192.168.0.0/16
    (255.255.0.0)
  10.0.0.0/8
  172.16.0.0/12
  172.31.0.0/12
  192.168.0.0/24
  192.168.255.0/24
  127.0.0.0
NAT(Network Address Translation)
BLM3051
Data Communication and Computer Network - 12
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 7: Thank you for your listening.
BLM3051
Data Communication and Computer Network - 12
Dr. Öğr. Üyesi Furkan ÇAKMAK