## Slide 1: Data Communication and Computer Network BLM3051
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 2: Lecture Information Form - Weekly Subjects
Hafta | Tarih | Konular
1 | 20.02.2024 | Introduction to Data Communication Standards Used on Data Communication, Architectural models
2 | 27.02.2024 | OSI Reference Model , Layers and Their Functions, Signaling and Signal Encoding
3 | 05.03.2024 | Parallel and Serial Transmission, Communication Media and Their Technical Specs., Multiplexing (TDM, FDM)
4 | 12.03.2024 | Error Detection and Error Correction Techniques, Data Link Control Techniques, Flow Control
5 | 19.03.2024 | Asynchronous and Synchronous Data Link Protocols (BSC, HDLC)
6 | 26.03.2024 | LAN Technologies Continued, IEEE 802.4, 802.5, 802.11
7 | 02.04.2024 | Connectionless and Connection Oriented Services, Switching
8 | 09.04.2024 | Tatil – Ramazan Bayramı Arifesi
9 | 16.04.2024 | 1. Ara Sınav
10 | 23.04.2024 | Tatil – 23 Nisan Ulusal Egemenlik ve Çocuk Bayramı
11 | 30.04.2024 | Static and Dynamic Routing, Congestion in the Network Layer, Its Causes and Solutions
12 | 07.05.2024 | IP (Internetworking Protocol), ICMP, BOOTP, DHCP
13 | 14.05.2024 | 2. Ara Sınav
14 | 21.05.2024 | UDP (User Datagram Protocol), TCP (Transmisson Control Protocol)
Dr. Öğr. Üyesi Furkan ÇAKMAK
BLM3051
Data Communication and Computer Network - 14

## Slide 3: Transport Layer
The Internet
  UDP (User Datagram Protocol)
  TCP (Transmission Control Protocol)
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 4: UDP (User Datagram Protocol)
A Connectionless Protocol
Nothing beyond sending pack- ets between applications.
  Letting applications build their own protocols on top
Sending datagrams
UDP transmits segments consisting of an 8-byte header
Using only raw IP, not ports
  So, the transport layer would not know what to do with each incoming packet.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
16-bits | 16-bits | 16-bits | 16-bits
Source Port | Destination Port | UDP length | UDP checksum
UDP Header

## Slide 5: UDP (User Datagram Protocol) (Con’t)
The IPv4 pseudoheader (in IP layer, we are in transport layer)
  Source and destionation address is 32-bits
  No checksum (00000000)
  Protocol = 17
  UDP length: 16-bits
UDP does not do
  Flow control
  Congestion control
  Retransmission
UPD does do
  Optional end-to-end error detection (with Checksum)
  An interface to the IP protocol with the added feature of demultiplexing multiple processes using the ports
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 6: UDP (User Datagram Protocol) (Con’t)
DNS (Domain Name System) uses UDP
  www.ce.yildiz.edu.tr
Remote Procedure Call
  Not traditional function call
  Client – Server relationship
    The calling procedure is known as the client
    The called procedure is known as the server
  Client stub: represents the server procedure in the client’s address space.
    Packing the parameters is called marshaling.
  Similarly, the server is bound with a procedure called the server stub.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 7: UDP (User Datagram Protocol) (Con’t)
Real-Time Transport Protocols
  For real-time multimedia applications.
    Internet radio,
    Internet telephony,
    Music-on-demans,
    Videoconferencing,
    Video-on-demand.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 8: UDP (User Datagram Protocol) (Con’t)
Jitter and Buffer relationship
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 9: Transport Layer
The Internet
  UDP (User Datagram Protocol)
  TCP (Transmission Control Protocol)
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 10: TCP (Transmission Control Protocol)
UDP is a simple protocol
  But for most Internet applications, reliable, sequenced delivery is needed
TCP
  is a reliable end-to-end byte stream over an unreliable internetwork.
  defined in September 1981.
  Extensions for high-performance
  Selective acknowledgements
  Congestion control
  Repurposing of header fields for quality of service
  Improved retransmission timers
  Explicit congestion notification
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK

## Slide 11: TCP (Transmission Control Protocol) (Con’t)
Well-known ports:
  Port numbers below 1024 are reserved for standard services
    Over 700 have been assigned.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
Port | Protocol | Use
20, 21 | FTP | File transfer
22 | SSH | Remote login, replacement for Telnet
25 | SMTP | Email
80 | HTTP | World Wide Web
110 | POP-3 | Remote email access
143 | IMAP | Remote email access
443 | HTTPS | Secure Web (HTTP over SSL/TLS)
543 | RTSP | Media player control
631 | IPP | Printer sharing

## Slide 12: TCP (Transmission Control Protocol) (Con’t)
All TCP connections are full duplex and point-to-point.
  TCP does not support multicasting or broadcasting.
A TCP connection is a byte stream, NOT a message stream.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 13: TCP (Transmission Control Protocol) (Con’t)
The TCP Segment Header
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 14: TCP (Transmission Control Protocol) (Con’t) The TCP Segment Header
TCP header size is 20 bytes.
IP header ize is 20 bytes.
65535-20-20 = 65,495 bytes data.
This connection identifier is called a 5 tuple
  The protocol (TCP)
  Source IP
  Source port
  Destination IP
  Destination port
TCP segments: 536 + 20 = 556 bytes
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK
*Andrew S. Tanenbaum - Computer Networks

## Slide 15: Thank you for your listening.
BLM3051
Data Communication and Computer Network - 14
Dr. Öğr. Üyesi Furkan ÇAKMAK